## Slide 1: How do i…? microscopy and cell counts
2015 Jan 16

## Slide 2: Your STEP by STEP guide to MICROSCOPY
Prep samples | most bacterial cells will require staining with SYBR or DAPI. Both stain nucleic acids
Prepare slides | filter stained samples on to black polycarbonate filters for best viewing and preserve slide with anti-fade solution
Onto the scope room!!
  JH 220A – can be accessed by JH key GM 174 (office key)
  Nikon with 10x, 40x, and 100x objectives

## Slide 5: Your STEP by STEP guide to Image processing
Login to computer and open software
  login: synechococcus password: ihatephage
Set working directory | create working directory:
  Username > date (YRMODA) > same name
    This is important for image processing later
  Set working directory in image capture software
    File > Options > directory name
    select “apply”
Capture images | generally use transect across filter and capture 10-20 images using AUTO
Transfer images to jump drive | The computer is not networked nor does it have the image processing software installed currently
Analyze images using ImageJ |Free software available for download to process images

## Slide 6: Your STEP by STEP guide to Cell enumeration
Save results as csv or enter into counting template
Use R code to calculate cellular density